## Slide 1: A 32-Bit Computer for LatticeXP2 Brevia Development Kit
Silicon Valley FIG
December 18, 2010
Chen-Hanson Ting

## Slide 2: Contents
1 eP32 Microprocessor
2 Design of eP32
3 eP32 Instructions
4 Implement eP32 on Brevia Kit
5 eP32 Chip Design in VHDL
6 Metacompilation of eP32

## Slide 3: Implement eP32 on Brevia Kit
Synthesis eP32
Simulate eP32
Layout eP32
Download eP32
Reveal eP32

## Slide 4: Synthesis eP32
Synplicity synthesis Tools
  ep32_chip.vhd
  ep32.vhd
  ram_memory.vhd
  uart.vhd
  gpio.vhd

## Slide 6: Synthesis eP32
Only ram_memory.vhd must be reconstructed to use RAM_Q modules in LatticeXP2-5E FPGA chip.
Ep32q.mem is produced by eForth metacompiler to initialize RAM_Q modules in XP2.

## Slide 7: Simulate eP32
Active-HDL simulation tools supplied by Aldec
Need a test bench module to test eP32 chip.
Activate ep32q_tb.vhd for functional simulation

## Slide 10: Layout eP32
Invoke Design Planner to connect following signals
  External reset
  External master clock
  Interrupts
  GPIO to LED and switches
  UART transmit
  UART receiver

## Slide 12: Download eP32
JTAP cable connected to printer port
UART cable connected to CMO port
Invoke ispVM system to download ep32_xp2.jed file
eP32 eForth signs on Hyperterminal

## Slide 15: Reveal eP32
Invoke Reveal Inserter to insert debugging logic and tracing memory
Invoke Synplicity to synthesize modified chip design
Download tp XP2 chip with ispVM
Invoke Reveal Logic Analyzer to trace selected internal signals

## Slide 19: Reveal eP32
Very powerful debugging tool
All signals in internal modules can be selected for tracing
Waveform display is like a super-expansive logic analyzer
It solved my reset problem in eP32.

## Slide 20: eP32_xp2 Preliminary Release
All VHDL design files
All eForth metacompiler files
weForth system files
This book in ep32_xp2.pdf

## Slide 21
Questions?

## Slide 22
Thank You.