## Slide 1: 328eForth for Arduino Uno
C. H. Ting
March 26, 2011
SVFIG

## Slide 2: Summary
eForth 1 Implementations
eForth 2 Implementations
ATmega328P
AmForth
328eForth v2.1
AVR Studio 4 Tool Suite
HyperTerminal
Bill Ragsdale’s Applications
eForth Tutorials
Conclusion

## Slide 3: eForth 1 Implementations
eForth Model in 8086
Direct Thread Model
30 Primitives
Ported to 8051, Z80, 8096/8098, 80386, 68000, 6805, 68HC11, 68HC12, 68HC16, Hitachi H8/532, MIPS, Power PC, Transputer, M56002, Java

## Slide 4: eForth 2 Implementations
Subroutine Thread Model
Optimized for performance
Potrted to 8051, 6805, 68HC12, Analog Devices AD2181, 80386, Philips 80C51XA, ADuC7020, Atmel AT91SAM7, STM8S105, eP32, C

## Slide 5: ATmega328P
8 Bit microcontroller, 131 instructions
20 MIPS at 20 MHz
32KB Flash, 2 KB RAM, 1 KB EEPROM
3 Counter/Timers
6 Channels 10-bit ADC
USART, SPI, I2C, ISP
23 Programmable I/O lines
1.8-5.5 V

## Slide 6: AmForth
NIH, Not Invented Here
Indirect Thread Model
Hundreds of little files
Inefficient flash programming
Cannot be simulated in AVR Studio 4, because of the IJMP instructions
All words are in lower case, and it is case sensitive
Strange error handling

## Slide 7: 328eForth v2.1
Subroutine Thread Model
Fully optimized
Uniform byte addressing
Case insensitive
Interpreter is in Bootloader section
Optimized flash programming
Visible words are reduced to 140 for ease of learning

## Slide 8: AVR Studio 4 Tool Suite
AVR Assembler 2
AVR Simulator 2
In System Programming with AVRISP mkll

## Slide 9: HyperTerminal
Arduino 0022 supplies USB to UART driver
19,200 Baud, 8 data bits, 1 stop bit, no parity, no flow control
900 ms delay after sending each line of text
Send Text File option to download file to Uno

## Slide 10: Bill Ragsdale’s Applications
Hello-world.txt
Marker.txt
Io-core.txt
Flasher.txt
Tone.txt
Keyer.txt
Chronometer.txt
Dump.txt

## Slide 11: eForth Tutorials
17 Tutorial lessons on
  Terminal interface
  Word games
  Math
  Calendar
  Sines and cosines
  Square root
  Random numbers
  Guess a number

## Slide 12: Conclusion
ISP is very pleasing
Flash memory in ATmega328 can endure 10,000 erase-write cycles
Ping-pong flash buffers optimize flash programming
2.1 us per empty FOR-NEXT loop at 16 MHz
ATmega328P is forced to be compatible with eForth

## Slide 13
Questions?

## Slide 14
Thank you.