## Slide 1: PDP1 Design Workshop
Silicon Valley
Forth Interest Group
June 25, 2016
Chen-Hanson Ting

## Slide 2: Summary
PDP1 Architecture
PDP1 Instruction set
FPGA Implementation
eForth Implementation
Demonstration
Discussions

## Slide 6: PDP1 Architecture
Von Neumann architecture
4096 18-Bit core memory
AC and IO registers
18 Bit instructions
  5-bit opcode
  1-bit indirection
  12-bit address

## Slide 8: PDP1 Instruction set
Memory reference instructions
  Arithmetic instructions
  Logic instructions
  General instructions
Augmented instructions
  Literal instruction
  Shift/rotate instructions
  Skip instructions
  Operate instructions

## Slide 9: PDP1 Instruction set

## Slide 10: ALU Instructions
add Y 40 add
sub Y 42 subtract
mus Y 54 multiply step
dis Y 56 divide step
idx Y 44 increment
isp Y 46 increment and skip if positive
and Y 2 logical and
xor Y 6 exclusive or
ior Y 4 inclusive or

## Slide 11: Register Instructions
lac Y 20 load accumulator
dac Y 24 deposit accumulator
dap Y 26 deposit address part
dip Y 30 deposit instruction part
lio Y 22 load in-out register
dio Y 32 load in-out register
dzm Y 34 deposit zero in memory

## Slide 12: Transfer Instructions
xct Y 10 execute
jmp Y 60 jump
jsp Y 62 jump and save program counter
cal Y 16 call subroutiine
jda Y 17 jump and deposit accumulator
sad Y 50 skip if accumulator and Y differ
sas Y 52 skip if accumulator and Y are the same

## Slide 13: Shift/Rotate Instructions
sza 640100 skip on zero accumulator
spa 640200 skip on plus accumulator
sma 640400 skip on minus accumulator
azo 641000 skip on zero overflow
spi 642000 skip on plus io register
szs 640010-640070 skip on zero switch
szf 640001-640007 skip of zero program flag

## Slide 14: PDP1 Instruction set

## Slide 15: Shift/Rotate Instructions
rar 671 rotate accumulator right
ral 661 rotate accumulator left
sar 675 shift accumulator right
sal 665 shift accumulator left
rir 672 rotate io register right
ril 662 rotate io register left
sir 676 shift io register right
sil 666 shift io register left
rcr 673 rotate ac and io right
rcl 663 rotate ac and io left
scr 677 shift ac and io right
scl 667 shift ac and io left

## Slide 16: PDP1 Instruction set

## Slide 17: Miscelaneous Instructions
iot 72nnnn Input-Output operations
law N 70nnnn load accumulator with N

## Slide 18: Deviations from PDP1
Indirection bit not allowed in memory
Memory can be incremented and decremented
Shift/Rotate one bit at a time
IO instructions use AC, not IO register
2’s complement arithmetic, not 1’s complement

## Slide 19: FPGA Implementation
Synthesis
Simulation
Programming
Debugging

## Slide 20: FPGA Implementation
Pdp1_chip.vhd
Pdp1.vhd
Uart1.vhd
Gpio.vhd
Pdp1.lpf

## Slide 25: eForth Implementation
Pdp1.fex
Meta_pdp1.f
Asm_pdp1.f
Kernel_pdp1.f
Ef_pdp1.f
Pdp1.mem

## Slide 29: Forth Virtual Machine on PDP1
Hardware registers: AC, IO
FVM registers: ac, ip, sp, rp, tos, tmp
Inner interpreters:
next: ip idx ip () jmp
doLIST
EXIT
doVAR
doCON

## Slide 30: eForth Inner Interpreter
22 CONSTANT sp
23 CONSTANT rp
24 CONSTANT ip
25 CONSTANT ac
26 CONSTANT tos
27 CONSTANT tmp

## Slide 31: eForth Inner Interpreter
next: ip idx ip () jmp
doLIST: ac dac rp ddx ip lac rp () dac
ac lac ip dac ip () jmp
EXIT: rp () lac ip dac rp idx next
doCON: ac dac pushs ac () lac tos dac next
doVAR: ac dac pushs ac lac tos dac next

## Slide 32: WORDS
:: WORDS ( -- )
CR CONTEXT
BEGIN @ ?DUP
WHILE DUP SPACE .ID
1-
REPEAT ;;

## Slide 33
2527 47522 42123 WORDS
620030 doLIST
602457 CR
600733 CONTEXT
BEGIN
600172 @
600520 ?DUP
600074 4341 WHILE
600235 DUP
602374 SPACE
604233 .ID
600367 1-
600063 4327 REPEAT
600125 EXIT

## Slide 35: Demonstrations
: TEST1 1 2 3 4 5 ;
: TEST2 CR .” HELLO, WORLD!” ;
: TEST3 IF 1 ELSE 2 THEN . ;
: TEST4 10 FOR R@ . NEXT ;
: TEST5 10 BEGIN DUP . DUP
WHILE 1- REPEAT DROP ;

## Slide 36: Demonstrations
HEX from octal
0 OUT turn on all LED’s
FE OUT turn on LED-1
IN read switches
IN read switches
IN read switches

## Slide 37: Last Words
The easiest way
to design a CPU
is
the eForth way.

## Slide 38
Questions?

## Slide 39
Thank you very much.